## Slide 1: Vortex Code Structure
Blaise Tine

## Slide 2: Agenda
Source Tree
Documentation
Hardware
Synthesis
Simulation
Runtime
Drivers
Testing and Integration
Configuration
Coding Convention
Multi-threading

## Slide 3: Source Tree
Reference: /vortex
/ci: Continuous integration
/doc Documentation
/hw Hardware
/runtime Runtime
/driver Drivers
/sim Simulation
/tests Testing

## Slide 4: Documentation
Reference: /vortex/doc
Vortex.md
  Codebase Layout
  Microarchitecture
  Cache Subsystem
  Software
  Simulation
  FPGA Setup Guide
  Debugging

## Slide 5: Hardware
Reference: /vortex/hw
/dpi Verilog DPI library
/scripts Scripting tools
/syn Synthesis tree
/unit_tests Hardware unit tests

## Slide 6: Hardware - RTL
Reference: /vortex/rtl
/afu Command processor
/cache Cache source tree
/fp_cores floating-point cores
/tex_unit Texture unit
/interfaces Module interfaces
/libs Library modules

## Slide 7: Hardware – Processor Dependency Tree
vortex
cluster
core
cluster
cluster
core
core
pipeline
mem_unit
sharedmem
dcache
issue
fetch
decode
execute
commit
scheduler
icache
ibuffer
scoreboad
GPR
writeback
alu_unit
lsu_unit
fpu_unit
csr_unit
gpu_unit

## Slide 8: Hardware – AFU
AFU
cci_to_mem
avs_wrapper
vortex
vx_to_mem
scope
Reference: /vortex/rtl/afu
vortex: Main processor
vx_to_mem: Vortex request
cci_to_mem: PCIe request
avs_wrapper: Avalon request
scope: Scope analyzer

## Slide 9: Hardware – Cache
cache
bank
bank_sel
tag_access
flush_ctrl
data_access
mshr
rsp_merge
nc_bypass
Reference: /vortex/rtl/cache
nc_bypass: cache bypassing
flush_ctrl: flushing
bank_sel: bank select
rsp_merge: response merge

## Slide 10: Synthesis
Reference: /vortex/hw/syn
/opae Intel OPAE FPGA synthesis
/quartus Intel Quartus synthesis
/yosys Yosys
/synopsys Synopsys
/modelsim Modelsim

## Slide 11: Simulation
Reference: /vortex/sim
/rtlsim Processor RTL simulator
/vlsim AFU + Processor RTL simulator
/simX Cycle-level simulator

## Slide 12: Runtime
Reference: /vortex/runtime
/linker Loader scripts
/src Runtime API sources
  start.* Startup routine
  print.* Standard out print
  spawn.* Tasks scheduler
  perf.* Performance counter logger
  syscalls.* System calls handling

## Slide 13: Driver
Reference: /vortex/driver
/stub Stub library for applications
/fpga OPAE FPGA driver
/asesim OPAE simulation driver
/vlsim VLSIM driver
/rtlsim RTLSIM driver
/simX SimX driver

## Slide 14: Testing - Coverage
Reference: /vortex/tests
/runtime Runtime tests
/regression C++ applications tests
/opencl OpenCL benchmarks
/riscv RISC-V standard tests

## Slide 15: Testing - Integration
Reference: /vortex/ci
blackbox.sh Vortex apps runner
regression.sh CI regression suite
Test_compiler.sh CI compiler suite
prebuild.sh Build prebuilt binaries
toolchain_install.sh Install prebuild binaries
Usage: <tool> --help

## Slide 16: Configuration - VX_config.vh
Reference: /vortex/hw/rtl/VX_config.vh
Contains all HW configuration parameters
  e.g. NUM_CORES, NUM_THREADS, L2_ENABLE
Autogen C++ header: VX_config.h
  $ make –s

## Slide 17: Configuration – VX_config.vh (2)
Structure
Memory

## Slide 18: Configuration – VX_config.vh (3)
Structure
Memory
CSRs
Caches

## Slide 19: Configuration - Software
Reference: /vortex/hw/VX_config.h
Consumed by all SW components
  Vortex Runtime
  All simulators
Blackbox examples:
  ./ci/blackbox.sh --cores=2 --warps=2 --threads=8 –app=vecadd
  CONFIGS=“-DNUM_CORES=2 -DDNUM_BANKS=1“ ./ci/blackbox.sh --app=sgemm
  CONFIGS="-DMEM_LATENCY=100“ ./ci/blackbox.sh --app=demo

## Slide 20: Configuration - Synthesis
Reference: /vortex/hw/syn/opae
FPGA build scripts allows customization
  Use parameters from VX_config.vh
FPGA synthesis examples:
  CONFIGS="-DNUM_THREADS=4“ make fpga-4c
  CONFIGS="-DNUM_WARPS=4“ make fpga-4c
  CONFIGS=“-DPERF_ENABLE=4“ make fpga-4c

## Slide 21: Coding Convention - Interfaces
Reference: /vortex/hw/rtl/interfaces
Grouping of related signals
Master/slave interconnect
  Master: outgoing
  Slave: incoming

## Slide 22: Coding Convention – Handshaking
Elastic Pipeline Pattern
valid/ready interfaces
  out: data Data to transfer
  out: valid Producer has valid data to transfer
  in: ready Consumer is ready to accept data
fire => valid && ready;

## Slide 23: Coding Convention – Naming
Benefits of coding standard
  Self-documentation
  Refactoring
  Extensibility
Module files: VX_<module>.sv
Interfaces: VX_<interface>_if.sv
Header: VX_<name>.vh
Data Types: VX_<name>_types.vh

## Slide 24
Thank You!